## Slide 1
LAB 41
SOAP namespaced purchase order to canonical JSON
Show the failing starter first. Hold the pause card before any solution.
hard · 8–12 min · LAB-41-soap-namespaced-purchase-order-to-canonical-json.mp4
Notes: Open PowerPoint Slide Show (F5). Share this window. Switch to Playground on code slides.

## Slide 2
LAB 41
The job
• This is Lab 41. SOAP namespaced purchase order to canonical JSON. Strip SOAP envelope, read ord:PurchaseOrder attributes and repeating ord:Line attributes.
• Two prefixes. This is a standard hard XML interview.
• Two ns prefixes. Envelope Body PurchaseOrder. Star Line. Attributes with at-sign.
Notes: This is Lab 41. SOAP namespaced purchase order to canonical JSON. Strip SOAP envelope, read `ord:PurchaseOrder` attributes and repeating `ord:Line` attributes. Two prefixes. This is a standard hard XML interview. Two ns prefixes. Envelope Body PurchaseOrder. Star Line. Attributes with at-sign.

## Slide 3
LAB 41
Paste the payload
• Set the MIME type to match the sample.

## Slide 4
LAB 41
Input
<soap:Envelope xmlns:soap="http://schemas.xmlsoap.org/soap/envelope/" xmlns:ord="http://acme.com/order">
<soap:Body>
<ord:PurchaseOrder id="PO-1001" currency="INR">
<ord:Line sku="SKU-A" qty="2" unitPrice="50.00"/>
<ord:Line sku="SKU-B" qty="1" unitPrice="100.00"/>
</ord:PurchaseOrder>
</soap:Body>
</soap:Envelope>
Notes: Type this. Read the header: percent dw two point oh, output, dash dash dash.

## Slide 5
PAUSE CARD
Pause — try Lab 41
• Pause the video
• Open student/labs/03-advanced/41-soap-namespaced-purchase-order-to-canonical-json/
• Finish transform.dwl — wrong is fine
• Resume when you have an attempt
Notes: Hold 3–5 seconds. Do not show the solution yet.

## Slide 6
LAB 41
Welcome back
• Welcome back. I will type the reference script. Follow along; do not paste blindly. Header first: percent dw two point oh, output, dash dash dash.
• That should match Expected:

## Slide 7
LAB 41
Solution
%dw 2.0
ns soap http://schemas.xmlsoap.org/soap/envelope/
ns ord http://acme.com/order
output application/json
---
{
orderId: payload.soap#Envelope.soap#Body.ord#PurchaseOrder.@id,
currency: payload.soap#Envelope.soap#Body.ord#PurchaseOrder.@currency,
lines: payload.soap#Envelope.soap#Body.ord#PurchaseOrder.*ord#Line map {
sku: $.@sku,
qty: $.@qty as Number,
unitPrice: $.@unitPrice as Number
}
}
Notes: Type this. Read the header: percent dw two point oh, output, dash dash dash.

## Slide 8
LAB 41
Expected
{
"orderId": "PO-1001",
"currency": "INR",
"lines": [
{ "sku": "SKU-A", "qty": 2, "unitPrice": 50.00 },
{ "sku": "SKU-B", "qty": 1, "unitPrice": 100.00 }
]
}
Notes: Type this. Read the header: percent dw two point oh, output, dash dash dash.

## Slide 9
LAB 41
Interview phrase
• Two ns prefixes. Envelope Body PurchaseOrder. Star Line. Attributes with at-sign.
• If your output differs, check plus versus plus-plus, as Number, and nulls with default. Next lab is the next numbered folder.
• Stop. Do not start Lab 42 in this file.
Notes: Two ns prefixes. Envelope Body PurchaseOrder. Star Line. Attributes with at-sign. If your output differs, check plus versus plus-plus, as Number, and nulls with default. Next lab is the next numbered folder. Stop. Do not start Lab 42 in this file.