## Slide 1
LAB 50
Tree map: apply f to every leaf string
Show the failing starter first. Hold the pause card before any solution.
hard · 8–12 min · LAB-50-tree-map-apply-f-to-every-leaf-string.mp4
Notes: Open PowerPoint Slide Show (F5). Share this window. Switch to Playground on code slides.

## Slide 2
LAB 50
The job
• This is Lab 50. Tree map: apply f to every leaf string. Uppercase every string leaf; leave numbers as-is. Same recursion skeleton as PII mask.
• Tree map: same recursion as mask, apply f to every string leaf.
Notes: This is Lab 50. Tree map: apply `f` to every leaf string. Uppercase every string leaf; leave numbers as-is. Same recursion skeleton as PII mask. Tree map: same recursion as mask, apply f to every string leaf.

## Slide 3
LAB 50
Paste the payload
• Set the MIME type to match the sample.

## Slide 4
LAB 50
Input
{ "a": "ok", "b": 2, "c": ["wait", 3] }
Notes: Type this. Read the header: percent dw two point oh, output, dash dash dash.

## Slide 5
PAUSE CARD
Pause — try Lab 50
• Pause the video
• Open student/labs/03-advanced/50-tree-map-apply-f-to-every-leaf-string/
• Finish transform.dwl — wrong is fine
• Resume when you have an attempt
Notes: Hold 3–5 seconds. Do not show the solution yet.

## Slide 6
LAB 50
Welcome back
• Welcome back. I will type the reference script. Follow along; do not paste blindly. Header first: percent dw two point oh, output, dash dash dash.
• That should match Expected:
• { "a": "OK", "b": 2, "c": ["WAIT", 3] }

## Slide 7
LAB 50
Solution
%dw 2.0
output application/json
fun mapLeaves(x) =
x match {
case s is String -> upper(s)
case a is Array -> a map mapLeaves($)
case o is Object -> o mapObject ((v, k) -> { (k): mapLeaves(v) })
else -> x
}
---
mapLeaves(payload)
Notes: Type this. Read the header: percent dw two point oh, output, dash dash dash.

## Slide 8
LAB 50
Interview phrase
• Tree map: same recursion as mask, apply f to every string leaf.
• If your output differs, check plus versus plus-plus, as Number, and nulls with default. Next lab is the next numbered folder.
• Stop. Do not start Lab 51 in this file.
Notes: Tree map: same recursion as mask, apply f to every string leaf. If your output differs, check plus versus plus-plus, as Number, and nulls with default. Next lab is the next numbered folder. Stop. Do not start Lab 51 in this file.